## Slide 1: Update on BRSKI with Pledge in Responder Mode (BRSKI-PRM)
draft-ietf-anima-brski-prm-18
Repo URL: https://github.com/anima-wg/anima-brski-prm
Steffen Fries, Thomas Werner, Elliot Lear, Michael Richardson
Shepherd: Matthias Kovatsch
IETF 122 – ANIMA Working Group

## Slide 2: BRSKI-PRM History of main changes 15 18
Alignment with latest version of JWS-voucher
Specific comments from several expert reviews in preparation of IESG evaluation led to
  AD review: Enhancements to terminology; Section 8 and Section 11 added more detailed recommendations for logging; new Section 9 to outline operational considerations; Section 12.3 added details regarding misuse of Registrar-Agent
  IANA expert review: included registered service names in headings
  IOTDIR review: clarification regarding minimum supported discovery approach
  SECDIR review: included reasoning for using short lived certificates and optional use of TLS; added hint for handling if the accept header is not used and additional hints for response body encoding;
Various nits addressed from AD/DNSDIR/GenArt/IOTDIR/OPSDIR reviews
3/11/2025
2

## Slide 3: BRSKI-PRM Status & Next Steps
Status: IESG Evaluation
On telechat agenda for April 17
Further Interop testing with other parties welcome , PoC implementations of all components available, please get in touch
3
3/11/2025

## Slide 4: Backup: BRSKI-PRM – Abstract Protocol Overview
4
Trigger Voucher-request { {reg-cert, agent-signed-data}
Pledge-Voucher-Request (PVR) {S/N, reg-cert, agent-signed-data, …}
Pledge-Voucher-Request {S/N, reg-cert, …}
S/N verification
Verification „reg-cert“ in voucher is own cert
Registrar-Voucher-Request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Verification of “agent-signed-cert” and “agent-signed-data”
Issues voucher with assertion agent-proximity
Voucher {reg-cert, assertion, …}
Voucher {LDevID(Reg), assertion, …}, signed
Basement no connectivity to backend
Pledge (callee)
Registrar-Agent
Domain Registrar
RA
Domain CA
MASA
Trigger Enrollment-request
Pledge-Enrollment-Request (PER) {signature-wrapped CSR}
Voucher {reg-cert, assertion, …}, signed
Voucher-status
Enrollment-response {LDevID cert}
Enrollment-status
Pledge-Enrollment-Request (CSR)
Enrollment-response (LDevID cert)
IDevID
Manufacturer trust anchor
LDevID (RegAgt)
LDevID Cert (Reg)
S/N Pledge
LDevID (Reg)
IDevID Cert CA
S/N Pledge
Domain CA credentials
MASA credentials
Step1: Collect Bootstrapping request information from pledge
Step2: Infrastructure Interaction based on BRSKI approach to collect voucher and LDevID Cert
Step3: Provisioning of voucher, CA certs, and LDevID cert to pledge
First floor, connectivity to backend
Device audit log
Voucher status
Enrollment status
Provisional accept of registrar certificate
Issue operational certificate for pledge for target domain
Request CA certificates
CA Certificates, signed
Request CA certificates
CA certificates
CA Certificates, signed