## Slide 1: Update on BRSKI with Pledge in Responder Mode (BRSKI-PRM)
draft-ietf-anima-brski-prm-05
Repo URL: https://github.com/anima-wg/anima-brski-prm
Steffen Fries, Thomas Werner, Elliot Lear, Michael Richardson
IETF 115 – ANIMA Working Group

## Slide 2: BRSKI-PRM – Abstract Protocol Overview
2
Trigger Voucher-request { {reg-cert, agent-signed-data}
Pledge-Voucher-Request (PVR) {S/N, reg-cert, agent-signed-data, …}
Pledge-Voucher-Request {S/N, reg-cert, …}
S/N verification
Verification „reg-cert“ in voucher is own cert
Registrar-Voucher-Request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Verification of “agent-signed-cert” and “agent-signed-data”
Issues voucher with assertion agent-proximity
Voucher {reg-cert, assertion, …}
Voucher {LDevID(Reg), assertion, …}, signed
Basement no connectivity to backend
Pledge (callee)
Registrar-Agent
Domain Registrar
RA
Domain CA
MASA
Trigger Enrollment-request
Pledge-Enrollment-Request (PER) {signature-wrapped CSR}
Voucher {reg-cert, assertion, …}, signed
Voucher-status
Enrollment-response {LDevID cert}
Enrollment-status
Pledge-Enrollment-Request (CSR)
Enrollment-response (LDevID cert)
IDevID
Manufacturer trust anchor
LDevID (RegAgt)
LDevID Cert (Reg)
S/N Pledge
LDevID (Reg)
IDevID Cert CA
S/N Pledge
Domain CA credentials
MASA credentials
Step1: Collect Bootstrapping request information from pledge
Step2: Infrastructure Interaction based on BRSKI approach to collect voucher and LDevID Cert
Step3: Provisioning of voucher, CA certs, and LDevID cert to pledge
First floor, connectivity to backend
Device audit log
Voucher status
Enrollment status
Provisional accept of registrar certificate
Issue operational certificate for pledge for target domain
Request CA certificates
CA Certificates, signed
Request CA certificates
CA certificates
CA Certificates, signed

## Slide 3: BRSKI-PRM Status History of main changes 04 05
Enhancements
  Issues #32 and #49: Included registrar signature on voucher as mandatory. Provides PoP of registrars private key to pledge and ends provisional accept of the registrar certificate.
  Issue #35: Defined new endpoint for pledge (bootstrapping) status inquiry. Allows registrar-agent to query status of pledge (results in factory-default, voucher-success/error, enroll-success/error, connect-success/error).
  Issue #39 and #64: Enhanced error codes to allow a more fine grained error handling.
  Issue #47 and #36: MASA verification of LDevID(RegAgt) to the same LDevID(Reg) domain CA to ensure registrar-agent and registrar are under the same administrative control. Domain CA cert needed on MASA to verify LDevID(RegAgt) and LDevID(Reg), to issue voucher with assertion “agent-proximity”
  Issue #59: Enhanced security considerations and privacy considerations.
  Issue #70: Registrar-Agent Certificate removed from pledge trigger (was optional) and only contained in RVR. Saves bandwidth and simplifies the handling (less options).
11/3/2022
3

## Slide 4: BRSKI-PRM Status History of main changes 04 05
Clarifications/Editorial improvements
  Issue #27: Reworked terminology of "enrollment object", "certification object", "enrollment request object".  utilized rather short forms like PER, PVR, etc.
  Issue #31: clarified that combined pledge may act as client/server for further (re)enrollment
  Issue #42: clarified that registrar needs to verify the pledge status responses and ensure that they match the audit log response from the MASA, otherwise it needs drop the pledge and revoke the already issued certificate for the pledge.
  Issue #43: clarified that the pledge shall use the created-on time from the PVR-trigger object if the time has not been synchronized, yet.
  Issue #65: Removed reference to CAB Forum as not needed for BRSKI-PRM specifically.
  Reworked all object representations (prototypes) to align with JSON encoding
  Included examples for several objects in Appendix A (included size information. Issue #33)
11/3/2022
4

## Slide 5: BRSKI-PRM Status Next Steps
Clarification on YANG usage (together with other ANIMA documents)
Interop testing with others welcome , PoC implementations of all components available, please get in touch
Document shepherd (still) needed
Authors agree the document is ready for WGLC
11/3/2022
5