## Slide 1: Update on BRSKI with Pledge in Responder Mode (BRSKI-PRM)
draft-ietf-anima-brski-prm-10
Repo URL: https://github.com/anima-wg/anima-brski-prm
Steffen Fries, Thomas Werner, Elliot Lear, Michael Richardson
Shepherd: Matthias Kovatsch
IETF 118 – ANIMA Working Group

## Slide 2: BRSKI-PRM Status History of main changes 09 10
Addressed remaining issues from WGLC (03/2023) and design team discussions.
Most issues related to clarifications of terminology and call flow descriptions
Technical issues clarified:
  Included conflict resolution in mDNS and GRASP (Issue #93, Section 5.3.2)
  Enhanced host header processing on pledge site (issue #120, Section 5.2)
  Clarified availability of serial number information on domain registrar for pledge authorization (issue #122, Section 6.1)
  Clarified usage of alternative voucher formats (issue #123, Section 6.2.3)
  Removed strength comparison for voucher assertions (issue #125, Section 5.1 + 6)
11/3/2023
2
Notes: #79, clarified discovery in the context of BRSKI-PRM and included information about future discovery enhancements in a separate draft in Section 5.3.1.
#93, included information about conflict resolution in mDNS and GRASP in Section 5.3.2
#103, included verification handling for the wrapped CA certificate provisioning in Section 6.3.3
#106, included additional text to elaborate more the registrar status handling in Section 6.3.6
#116, enhanced DoS description in Section 10.1
#120, included statement regarding pledge host header processing in Section 5.2
#122, availability of serial number information on registrar agent clarified in Section 6.1
#123, Clarified usage of alternative voucher formats in Section 6.2.3
#124, determination of pinned domain certificate done as in RFC 8995 included in Section 6.2.4
#125, remove strength comparison of voucher assertions in Section 5.1 and Section 6
#130, aligned the usage of site and domain throughout the document
changed naming of registrar certificate from LDevID(RegAgt) to EE (RegAgt) certificate throughout the document
change x5b to x5bag according to [RFC9360]
updated JSON examples -> "signature": BASE64URL(JWS Signature)

## Slide 3: BRSKI-PRM, Open Issue #79 Discovery of registrar with BRSKI-PRM feature set
Discovery of registrar by and registrar-agent is not needed (have trust relation and are assumed to exchange upfront information).
Current discovery in BRSKI does not consider registrars with enhanced feature sets. This is handled in ID BRSKI-Discovery.
Proposal to keep simple assumption in BRSKI-PRM and refer to BRSKI-Discovery for cases, in which the enhanced discovery of a registrar by a registrar-agent is described (considering, e.g., the mode of operation or voucher formats, or others)
3
11/3/2023

## Slide 4: BRSKI-PRM, Open Issue #130 Discovery of pledges by a registrar-agent
Discovery of pledges by a registrar-agent described in two ways:
  "product-serial-number._brski-pledge._tcp.local", to discover a specific pledge.
  "_brski-pledge._tcp.local" to discover available pledges for bootstrapping.
ID BRSKI-Discovery describes more versatile approach to contain additional info (like manufacturer) to product serial number.
Proposal to keep simple discovery in BRSKI-PRM by using manufacturer-specific product serial numbers only.
  Note: May result in false positives (every manufacturer has serial number 001), the registrar-agent can filter through the results, e.g., based on the related IDevID CA certificate.
4
11/3/2023

## Slide 5: BRSKI-PRM Status Next Steps
Finalize open issues #79 and #130 (see ANIMA git)
WGLC done before IETF 116
IOT DIR early review done
SECDIR early review to be updated
Shepherd writeup
Ready for AD review
Interop testing with others welcome , PoC implementations of all components available, please get in touch
5
11/3/2023

## Slide 6: Backup: BRSKI-PRM – Abstract Protocol Overview
6
Trigger Voucher-request { {reg-cert, agent-signed-data}
Pledge-Voucher-Request (PVR) {S/N, reg-cert, agent-signed-data, …}
Pledge-Voucher-Request {S/N, reg-cert, …}
S/N verification
Verification „reg-cert“ in voucher is own cert
Registrar-Voucher-Request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Verification of “agent-signed-cert” and “agent-signed-data”
Issues voucher with assertion agent-proximity
Voucher {reg-cert, assertion, …}
Voucher {LDevID(Reg), assertion, …}, signed
Basement no connectivity to backend
Pledge (callee)
Registrar-Agent
Domain Registrar
RA
Domain CA
MASA
Trigger Enrollment-request
Pledge-Enrollment-Request (PER) {signature-wrapped CSR}
Voucher {reg-cert, assertion, …}, signed
Voucher-status
Enrollment-response {LDevID cert}
Enrollment-status
Pledge-Enrollment-Request (CSR)
Enrollment-response (LDevID cert)
IDevID
Manufacturer trust anchor
LDevID (RegAgt)
LDevID Cert (Reg)
S/N Pledge
LDevID (Reg)
IDevID Cert CA
S/N Pledge
Domain CA credentials
MASA credentials
Step1: Collect Bootstrapping request information from pledge
Step2: Infrastructure Interaction based on BRSKI approach to collect voucher and LDevID Cert
Step3: Provisioning of voucher, CA certs, and LDevID cert to pledge
First floor, connectivity to backend
Device audit log
Voucher status
Enrollment status
Provisional accept of registrar certificate
Issue operational certificate for pledge for target domain
Request CA certificates
CA Certificates, signed
Request CA certificates
CA certificates
CA Certificates, signed