## Slide 1: Update on BRSKI with Pledge in Responder Mode (BRSKI-PRM)
draft-ietf-anima-brski-prm-14
Repo URL: https://github.com/anima-wg/anima-brski-prm
Steffen Fries, Thomas Werner, Elliot Lear, Michael Richardson
Shepherd: Matthias Kovatsch
IETF 120 – ANIMA Working Group

## Slide 2: BRSKI-PRM History of main changes 12 13
Interim ANIMA Meeting: Clarification of CDDL usage, when no YANG definition is available for objects to use the description consistently
Update of Examples in Annex A (1 (PVR), 2 (RVR), 4 (Voucher)) to match definitions in draft
Clarification included when pledge has no synchronized clock in Section 7.2.2 (use of advanced created-on time from the agent-signed-data in PER)
Updated RVR to contain idevid-issuer as described in RFC 8995 in Section 7.3.2
7/23/2024
2
Notes: Deleted figure in Section "Request Artifact: Pledge Voucher-Request Trigger (tPVR)" for JSON representation of tPVR, as it has been replaced by CDDL
Updated reason-content description in status response messages (enroll-status, voucher-status, and status-response).
Updated CDDL source code integration to allow for automatic verification
Reordered description in Section 7.3 in Section 7.2 to better match the order of communication and artifact processing.
Updated CDDL for the request-enroll trigger in Figure 15 according to the outcome of the interim ANIMA WG meeting discussions on April 19, 2024
Included statement in Section 7.2.2 for using the advanced created-on time from the agent-signed-data also for the PER, when the pledge has no synchronized clock
Update of the examples in Appendix A to align with the defined prototypes
Changes incorporated based on Shepherd review PR #133:
  Terminology alignment and clarification throughout the document to use terms more consistently
  Restructuring of section Section 7 for protocol steps to align to the general approach: Overview, data description, CDDL description (if necessary), JWS Header an Signature. This lead to some movement of text between existing and new subsections.
  Inclusion of new section on logging hints Section 8 to give recommendations on which events to be logged for auditing
  Enhancement of IANA considerations in Section 9 with values for the trigger messages and with an enhancement of the pledge status query and response to allow for a more flexible status inquiry and reporting

## Slide 3: BRSKI-PRM History of main changes 13 14
Part 3 of Shepherd Review by Matthias Kovatsch led to the following main changes
  Structural improvements of the document, terminology, and simplification
  New section 6.4 in the architecture overview to outline MASA requirements when supporting BRSKI-PRM similar to existing description for registrar and pledge
  Section 7 restructured to describe protocol steps following a general approach: Overview, Request Artifact, Response Artifact (resulted in shifting existing text)
  Alignment of pledge status response data across Section 7.6.2.1 (vStatus), Section 7.8.2.1 (eStatus), and Section 7.11.2.1 (pStatus) to allows similar processing.
  Inclusion of new section on logging hints Section 8 to give recommendations on which events to be logged for auditing
7/23/2024
3
Notes: Deleted figure in Section "Request Artifact: Pledge Voucher-Request Trigger (tPVR)" for JSON representation of tPVR, as it has been replaced by CDDL
Updated reason-content description in status response messages (enroll-status, voucher-status, and status-response).
Updated CDDL source code integration to allow for automatic verification
Reordered description in Section 7.3 in Section 7.2 to better match the order of communication and artifact processing.
Updated CDDL for the request-enroll trigger in Figure 15 according to the outcome of the interim ANIMA WG meeting discussions on April 19, 2024
Included statement in Section 7.2.2 for using the advanced created-on time from the agent-signed-data also for the PER, when the pledge has no synchronized clock
Update of the examples in Appendix A to align with the defined prototypes
Changes incorporated based on Shepherd review PR #133:
  Terminology alignment and clarification throughout the document to use terms more consistently
  Restructuring of section Section 7 for protocol steps to align to the general approach: Overview, data description, CDDL description (if necessary), JWS Header an Signature. This lead to some movement of text between existing and new subsections.
  Inclusion of new section on logging hints Section 8 to give recommendations on which events to be logged for auditing
  Enhancement of IANA considerations in Section 9 with values for the trigger messages and with an enhancement of the pledge status query and response to allow for a more flexible status inquiry and reporting

## Slide 4: Food for thoughts: Supporting .local name in IDevID
BRSKI-PRM uses http and relies on self-contained authenticated objects for the communication between the registrar-agent and the pledge
For privacy reasons TLS may be used for this link, making the pledge the TLS server.
BRSKI-PRM states (Annex B): Pledge can use its IDevID certificate to authenticate itself, but pledge does not have a FQDN, and hence cannot be identified by DNS name. Instead, a new mechanism is required, which authenticates the X520SerialNumber DN attribute that must be present in every IDevID.
As BRSKI-PRM uses mDNS to discover the pledge it may provide its local name to the registrar-agent. If IDevID contains the local name the registrar-agent can use this information during the authentication in the handshake without a new mechanism.
Note: .local is not an FQDN; CABF does not allow internal names in the dNSName
4
7/23/2024

## Slide 5: Food for thoughts: Multiple LDevID Provisioning (not BRSKI-PRM specific)
BRSKI and variants handle the provisioning of a generic LDevID, which can be used to manage further LDevIDs in the operational phase.
There may be cases for providing multiple LDevIDs during onboarding like:
  application specific certificates
  Handle handovers from domain 1 to domain 2 during installation and commissioning
Technically, this may be achieved once the generic LDevID is enrolled using CSR attribute request messages of the enrollment protocol (as defined in BRSKI) or trigger messages for the pledge (as defined in BRSKI-PRM)
Operational workflow discussions may be necessary: Should be used to enhance ID Operational Considerations for BRSKI Registrar.
5
7/23/2024

## Slide 6: BRSKI-PRM Status & Next Steps
WGLC before IETF 116 - DONE
IOT DIR early review - DONE
SECDIR early review – DONE
YANGDOCTORS early review – DONE
Shepherd review and writeup – DONE
Ready for AD review
Further Interop testing with other parties welcome , PoC implementations of all components available, please get in touch
6
7/23/2024

## Slide 7: Backup: BRSKI-PRM – Abstract Protocol Overview
7
Trigger Voucher-request { {reg-cert, agent-signed-data}
Pledge-Voucher-Request (PVR) {S/N, reg-cert, agent-signed-data, …}
Pledge-Voucher-Request {S/N, reg-cert, …}
S/N verification
Verification „reg-cert“ in voucher is own cert
Registrar-Voucher-Request {prior-signed-voucher, …}
S/N verification
Verification „reg-cert“ in prior-signed-voucher
Verification of “agent-signed-cert” and “agent-signed-data”
Issues voucher with assertion agent-proximity
Voucher {reg-cert, assertion, …}
Voucher {LDevID(Reg), assertion, …}, signed
Basement no connectivity to backend
Pledge (callee)
Registrar-Agent
Domain Registrar
RA
Domain CA
MASA
Trigger Enrollment-request
Pledge-Enrollment-Request (PER) {signature-wrapped CSR}
Voucher {reg-cert, assertion, …}, signed
Voucher-status
Enrollment-response {LDevID cert}
Enrollment-status
Pledge-Enrollment-Request (CSR)
Enrollment-response (LDevID cert)
IDevID
Manufacturer trust anchor
LDevID (RegAgt)
LDevID Cert (Reg)
S/N Pledge
LDevID (Reg)
IDevID Cert CA
S/N Pledge
Domain CA credentials
MASA credentials
Step1: Collect Bootstrapping request information from pledge
Step2: Infrastructure Interaction based on BRSKI approach to collect voucher and LDevID Cert
Step3: Provisioning of voucher, CA certs, and LDevID cert to pledge
First floor, connectivity to backend
Device audit log
Voucher status
Enrollment status
Provisional accept of registrar certificate
Issue operational certificate for pledge for target domain
Request CA certificates
CA Certificates, signed
Request CA certificates
CA certificates
CA Certificates, signed